## Slide 1: The Fighting Meerkats
Present the Gameboy!

## Slide 2: The Game
Gameboy running Tetris (almost)
It’s not finished (but it’s still fun)!
  Nintendo logo scrolls
  Ping noise plays
  Tetris starting credits appear
  Start screen shows up!
  Demo plays in fast motion!
Just a little further to go!

## Slide 3: The Design

## Slide 4: The CPU
Implementation:
  Multi-cycle microcoded design, Z80/8080 custom hybrid
  Interrupt module with 5 maskable interrupts
  On-board SRAM for high memory accesses separate from other modules (addresses above 0xFF80)
  Single-cycle asynchronous read memory interface

## Slide 5: The CPU
Testing:
  Testbench that runs GB80 assembly files through the CPU and an external emulator and compares the register outputs
  57 instruction-level test programs
  7 interrupt and functional test programs
  Bootstrap ROM
  Tetris
  Blargg test ROMs
  Xilinx sucks

## Slide 6: The Video Interface
Promised:
  A working GPU and framebuffer
Delivered:
  A broken framebuffer
  No GPU functionality
  No working DVI output to monitor

## Slide 7: The Video Interface
Plans for the future:
  Very quickly get DVI properly set up and displaying something
  Will probably use code from team Dragonforce
  Get a working framebuffer
  Understand how the GPU works
Revised schedule:
  By Wednesday get test image on monitor
  In two weeks have framebuffer fully functional
  About one month behind schedule

## Slide 8: The Audio Interface
Copied code from team Dragonforce
Added
  Full square wave functionality
    Length, volume, frequency control full supported and accurate
  Volume envelope, frequency sweep supported
  Amplitude control using rotary controller
  18 memory-mapped registers for CPU communication

## Slide 9: The Audio Interface
Fully functional though perhaps buggy
  Unit tested each function
  Can’t test more until Tetris works
Did not implement white noise or sound enabled flags
  Deemed relatively low importance

## Slide 10: The Cartridge Connector

## Slide 11: The Cartridge Connector
Fully functional ability to read game ROM
  Enough to play Tetris
SRAM accessible in theory
  Tetris does not have SRAM
Did not implement bank switching
  Only necessary for larger games

## Slide 12: Timers/DMA
Timer generates an interrupt on overflow
  Selectable frequencies
  Enable/Disable
  Adjustable overflow reset value
DMA module that copies sections of memory
  Roughly 8 times faster than CPU copying

## Slide 13: Memory
(Mostly) Generated with CoreGen
Block RAM
  8kB of work RAM
  8kB and then some of video RAM
1 MB of framebuffer (not a block RAM)
  Synthesizes in a finite amount of time
Verdict: block RAM is probably not necessary in our system

## Slide 14: User Input and Link Cable
NES interface still buggy
  Working to debug
Link cable not attempted
  Time crunch and all that… You know.
There’s still time!

## Slide 15: Problems
We can’t really play Tetris quite yet
ChipScope is a pain in the ass
The RHEL machines we’re using are completely unstable

## Slide 16: Goals
Wednesday: Gameplay!
Thursday: Link cable?
Friday: Other games??

## Slide 17: Conclusions
If your project involves implementing a CPU/using a buggy one…
  Find a new project
  Testing a buggy CPU requires understanding of it’s implementation (i.e. you’ve already implemented it)
  Implementing a CPU means it will be buggy and you will have to test it
  Takes a long, long time either way
If your project involves Xilinx…
  Install Windows on the lab machines
  Seriously, what the fuck is going on

## Slide 18: Conclusions
ChipScope, you are our only hope
Don’t take 18-349
  Ever
  For any reason
The Virtex-7-based VC707 is not a good board for this class
  Until someone writes a SystemVerilog HDMI driver
  Or buys an expansion board with GPIO, VGA, and an AC97 chip
You will never have enough time. Don’t even pretend.

## Slide 19: Negative Feedback
Too many lab handouts/presentations
Sound lab is ridiculously difficult unless you find Team Dragonforce’s code
Virtex-7 is useless for video/sound

## Slide 20: Positive Feedback
Self-driven course
Learn about interfacing with other people’s designs
  AC97, Chrontel DVI, Flash, Xilinx ChipScope/BlockRAM
  Cartridge, controller
It was a lot of fun
  Exciting to come into lab and work on something you love
Testing, testing, testing

## Slide 21: Comments/Questions?