## Slide 1: The Fighting Meerkats
Present the Gameboy

## Slide 2: The Game
Supposed to be Tetris
It’s not (but it’s still fun)!
  Nintendo logo scrolls
  Ping noise plays
  Tetris starting credits appear
  Grinding noises happen
Right now, the game is: debug the design using ChipScope
You can play if you want, just ask

## Slide 3: The Design

## Slide 4: The CPU
Implementation:
  Multi-cycle microcoded design, Z80/8080 custom hybrid
  Interrupt module with 5 maskable interrupts
  On-board SRAM for high memory accesses separate from other modules (addresses above 0xFF80)
  Single-cycle asynchronous read memory interface

## Slide 5: The CPU
Testing:
  Testbench that runs GB80 assembly files through the CPU and an external emulator and compares the register outputs
  57 instruction-level test programs
  7 interrupt and functional test programs
  Bootstrap ROM
  Tetris
  Blargg test ROMs
  Xilinx sucks

## Slide 6: The Video Interface
Promised:
  A working GPU and framebuffer
Delivered:
  A broken framebuffer
  No GPU functionality
  No working DVI output to monitor

## Slide 7: The Video Interface
Plans for the future:
  Very quickly get DVI properly set up and displaying something
  Will probably use code from team Dragonforce
  Get a working framebuffer
  Understand how the GPU works
Revised schedule:
  By Wednesday get test image on monitor
  In two weeks have framebuffer fully functional
  About one month behind schedule

## Slide 8: The Audio Interface
Copied code from team Dragonforce
Added full square wave functionality
  Accurate frequency control
  Amplitude control using rotary controller
“Coded” memory-mapped registers

## Slide 9: The Audio Interface
Promised:
  A working audio interface
Delivered:
  Proper configuration of the AC’97
  The ability to play square waves and sound files from flash
  Pseudo-code memory-mapped registers
  No frequency sweep, volume envelope, or white noise

## Slide 10: The Audio Interface
Plans for the future:
  Actually make memory-mapped registers
    Probably just “reg” variables
  Add functions for frequency sweep and volume envelope
Revised schedule:
  By the end of October:
    Have frequency sweep and volume envelope functions
    Have CPU interface with memory-mapped registers
  About two weeks behind schedule

## Slide 11: The Cartridge Connector

## Slide 12: The Cartridge Connector
Promised:
  A working cartridge interface with ability to read ROM
Delivered:
  Exactly that
  Full ROM access
  No bank switching
  Only conceptual access to SRAM

## Slide 13: The Cartridge Connector
Plans for the future:
  SRAM and bank switching are lower priority
Revised schedule:
  ROM is fully accessible
  Get Tetris working
  Test capability to access SRAM
  Then work on bank switching
  Ahead of schedule!

## Slide 14: Memory
(Mostly) Generated with CoreGen
Block RAM
  8kB of work RAM
  8kB and then some of video RAM
1 MB of framebuffer (not a block RAM)
  Synthesizes in a finite amount of time
Verdict: block RAM is probably not necessary in our system

## Slide 15: User Input and Link Cable
This doesn’t exist!
We never mentioned it!
Forget about it!

## Slide 16: Problems
We only get to the Tetris starting credits
ChipScope is a pain in the ass
The RHEL machines we’re using are completely unstable

## Slide 17: Goals
Wednesday: Start screen?
Thursday: Start screen
Next Monday: Possibly buggy gameplay

## Slide 18: Conclusions
If your project involves implementing a CPU/using a buggy one…
  Find a new project
  Testing a buggy CPU requires understanding of it’s implementation (i.e. you’ve already implemented it)
  Implementing a CPU means it will be buggy and you will have to test it
  Takes a long, long time either way
If your project involves Xilinx…
  Install Windows on the lab machines
  Seriously, what the fuck is going on

## Slide 19: Conclusions
ChipScope, you are our only hope
Don’t take 18-349
  Ever
  For any reason
The Virtex-7-based VC707 is not a good board for this class
  Until someone writes a SystemVerilog HDMI driver
  Or buys an expansion board with GPIO, VGA, and an AC97 chip

## Slide 20: Negative Feedback
Too many lab handouts/presentations
Sound lab is ridiculously difficult unless you find Team Dragonforce’s code
Virtex-7 is useless for video/sound

## Slide 21: Positive Feedback
Self-driven course
Learn about interfacing with other people’s designs
  AC97, Chrontel DVI, Flash, Xilinx ChipScope/BlockRAM
  Cartridge, controller
Testing, testing, testing

## Slide 22: Comments/Questions?